## Slide 1
TINY_LOGIC // 01
Tiny Logic: The Math of Tiny House Design
Architecture is geometry. In a tiny house, every inch counts. This project explores the math you need to design a tiny house on wheels.
If geometry is a tough subject for you, seeing how the math works with a real house design might help you see how the math works.
RAY_JANZEN

## Slide 2
Floor Plan Geometry
TINY_LOGIC // 02
Area and Perimeter
To maximize living space within road-legal limits, we calculate the floor area and perimeter to size the foundation.
Area = Length x Width
Permieter = Length of all walls added together
For a 12 foot long by 8.0 foot wide house:
Perimeter: 2(12 + 8) = 40 feet of wall framing
Area: 12 × 8 = 96 square feet
8 feet
12 feet
RAY_JANZEN

## Slide 3
The Roof Structure
TINY_LOGIC // 03
Pythagorean Theorem
Calculating the rafter length (hypotenuse) for a gabled roof allows us to order precision-cut lumber.
a2 + b2 = c2
42 + 32 = c2
16 + 9 = 25
c = √(25) = 5 feet per rafter.
b = 3 feet
a = 4 feet
c = 5 feet
RAY_JANZEN

## Slide 4
Energy vs. Volume
TINY_LOGIC // 04
Tiny houses are more efficient because their Cubic Volume is lower. This chart shows the BTU (British Thermal Units) heating requirements as the volume of the space increases.
Volume = length x width x height
Required BTUs = Volume x 20
To size our mini-split air conditioner, we calculate the cubic volume of the house. Our house is 12 feet long, 8 feet wide, and has an average interior height of 10 feet.
12 x 8 x 10 = 960 cubic feet. Multiplying by 20 BTUs per cubic foot means we need a 19,200 BTU heater. A 2,000 sq ft home requires over 320,000 BTUs!
RAY_JANZEN

## Slide 5
Physics of Towing
TINY_LOGIC // 05
10-15%
Target Tongue Weight percentage relative to total house weight for safe highway towing.
Center of Mass
Located roughly 55-60% of the way back from the front of the trailer bed.
GVWR
Gross Vehicle Weight Rating must exceed total load to prevent axle failure.
Finding the Center of Mass
To prevent trailer sway, the axles must be mounted between 55% and 60% of the way back from the front hitch. For a 12-foot house:
Minimum Distance: 12 feet x 0.55 = 6.6 feet
Maximum Distance: 12 feet x 0.60 = 7.2 feet
The center of the wheels must sit inside this 0.6-foot safe zone.
RAY_JANZEN

## Slide 6
Legal Road Constraints
TINY_LOGIC // 06
8.5'
MAXIMUM WIDTH
13.5'
MAXIMUM HEIGHT
The Inequality Constraint
To avoid a "wide load" permit, our design must satisfy the following mathematical inequality:
Width ≤ 8.5 feet
Height ≤ 13.5 feet
RAY_JANZEN

## Slide 7
Budget Modeling
TINY_LOGIC // 07
Total cost follows a linear model: y = mx + b, where b is the fixed trailer cost ($6,500) and m is materials per sq ft.
We can predict our budget using a linear equation. Our custom trailer has a fixed cost of $6,500. We estimate materials will cost $120 per square foot. For our 96 square foot home, the equation is:
y = 120(96) + 6500
y = 11520 + 6500
Total estimated cost = $18,020.
RAY_JANZEN

## Slide 8
Space Allocation
TINY_LOGIC // 08
Percentage Distribution
Note: Maximizing the living area improves the "perceived" square footage.
•
45% Living Area: Multi-functional space
•
25% Kitchen: High-efficiency appliances
•
15% Bathroom: Compact utility wet-room
•
15% Sleeping Loft: Vertical space utilization
RAY_JANZEN

## Slide 9
Materials
TINY_LOGIC // 09
Component | Metric / Measurement | Math Applied
Wall Studs | 140 pcs (2x4x8) | 16" on-center spacing
Insulation (Rockwool) | 1,200 Board Feet | Surface Area calculation
Windows | 7 Units (Varying Sizes) | Light-to-Floor Area Ratio
Solar Array | 3 Panels (400W each) | Daily kWh consumption model
RAY_JANZEN